## Slide 1
COSC 2406: Assembly Language Programming
Module 2
Spring 2022

## Slide 2: Chapter 12 (12.1)
Contents of the lecture slides are taken from the following textbook
Irvine, Kip R. Assembly Language for x86 Processor 7/e, 2015.

## Slide 3: Floating-Point Processing
Floating-Point Binary Representation
  IEEE Binary Floating-Point Representation
  The Significand
  The Exponent
  Creating the IEEE Representation
  Converting Decimal Fractions to Binary Reals

## Slide 4: Floating-Point Processing
IEEE Binary Floating-Point Binary Reals (Table 12-1)
  Single Precision
    32 bits
      1 bit for the sign,
      8 bits for the exponent, and
      23 bits for the fractional part of the significand.
  Double Precision
    64 bits
      1 bit for the sign,
      11 bits for the exponent, and
      52 bits for the fractional part of the significand.
  Double Extended Precision
    80 bits
      1 bit for the sign,
      16 bits for the exponent, and
      63 bits for the fractional part of the significand.

## Slide 5: Single-Precision Format
Sign (1 bit) | Exponent (8 bits) | Fraction (23 bits)

## Slide 6: Components
Sign Bit
  1 = negative
  0 = positive
Significand
  Value is based on weighted position
  121.121 = (1 x 102) + (2 x 101) + (1 x 100) + (1 x 10-1) + (2 x 10-2) + (1 x 10-3)
Exponent
  unsigned integer
  Bias (127 for single precision)

## Slide 7: Binary Floating-Point
Binary Floating Point | Decimal Fraction
101.11 | 5 3/4
1001.001 | 9 1/8
1000.01 | 8 1/4
1010.1 | 10 1/2
1011.111 | 11 7/8

## Slide 8: Binary Floating-Point
Binary Floating Point | Decimal Fraction
0.1 | 1/2
0.01 | 1/4
0.001 | 1/8
0.0001 | 1/16
0.00001 | 1/32

## Slide 9: Binary Floating-Point
1001.101

## Slide 10: The Exponent
Exponent | Biased (E+127) | Binary
+3 | 130 | 10000010
0 | 127 | 01111111
-12 | 115 | 01110011
+126 | 253 | 11111101
-2 | 125 | 01111101

## Slide 11: Binary Numbers Normalization
Normalized
Unnormalized
Unnormalized | Normalized
1001.1 | 1.0011 Х 23
11.11111 | 1.111111 Х 21
0.00101 | 1.01 Х 2-3
101010. | 1.01010 Х 25

## Slide 12: Real-Number Encodings
Normalizing finite numbers
Positive and Negative Infinity
NaNs
  Quiet
  Signaling

## Slide 13: Real-Number Encoding
Value | Sign Exponent Significand
Positive zero | 0 00000000 00000000000000000000000
Negative zero | 1 00000000 00000000000000000000000
Positive infinity | 0 11111111 00000000000000000000000
Negative infinity | 1 11111111 00000000000000000000000
QNaN | X 11111111 1XXXXXXXXXXXXXXXXXXXXXX
SNaN | X 11111111 0XXXXXXXXXXXXXXXXXXXXXX
Table 12-6

## Slide 14: Fractions to Binary Reals
Decimal Fraction | Factored As | Binary Real
1/2 | 1/2 | 0.1
1/4 | 1/4 | 0.01
3/4 | 1/2 + 1/4 | 0.11
1/8 | 1/8 | 0.001
7/8 | 1/2 + 1/4 + 1/8 | 0.111
1/16 | 1/16 | 0.0001
1/32 | 1/32 | 0.00001

## Slide 15: Example
Convert 0 10000010 01011000000000000000000 to Decimal

## Slide 16: Example
Convert 0 10000010 01011000000000000000000 to Decimal
The number is positive. As MSB is 0.
The unbiased exponent is binary 00000011, or decimal 3.
Combining the sign, exponent, and significand, the binary number is +1.01011 X 23.
The unnormalized binary number is +1010.11.
The decimal value is +10 3/4, or +10.75.

## Slide 17: Single-Precision to Decimal
If the MSB is 1, the number is negative; otherwise, positive.
The next 8 bits represent the exponent.
  Subtract binary 01111111 (decimal 127), producing the unbiased exponent.
  Convert the unbiased exponent to decimal.
The next 23 bits represent the significand.
  Notate a “1.”, followed by the significand bits.
  Trailing zeros can be ignored. Create a floating-point binary number, using the significand, the sign determined in step 1, and the exponent calculated in step 2.
Unnormalize the binary number produced in step 3.
  (Shift the binary point the number of places equal to the value of the exponent. Shift right if the exponent is positive or left if the exponent is negative.)
  From left to right, use weighted positional notation to form the decimal sum of the powers of 2 represented by the floating-point binary number.

## Slide 18: Real-Number Encoding
10.75

## Slide 19: Example
Convert 0 10000000 01111000000000000000000 to Decimal

## Slide 20: Summary
Binary floating-point number
  sign, significand, and exponent
  single precision, double precision, extended precision
0 and 1 can not represent all numbers
Positive and negative infinity
NaN